## Slide 1: Quality Control
Then and Now

## Slide 2: Uniformity and interchangeability
Products (or services) should have uniformity
Components of products (or services) should also be uniform
Interchangeability of parts is a great advantage in manufacturing and maintenance
One way to achieve this is through “specifications”
Specifications attempt to define what is “acceptable” which may or may not be “ideal”
The problem is variation
No two products are exactly alike
Notes: services can include people, the processes by which things get done, software or hardware, etc.
The author calls the spec approach the Engineering approach, this may not be entirely fair but………………..

## Slide 3: How to achieve uniformity?
Set specifications for products, parts (or services)
Specifications should primarily be a result of customer needs
Specifications are the result of the interplay between the supplier and the customer
Uniformity could be achieved by comparing the product to the specification
This is not really “uniformity”, it is really “within specification”
This approach relies on extensive sampling and testing
Product is acceptable (within specification) or unacceptable (outside specification)
Notes: for parts: viscosity, strength, works or not
for service: delivery time, service completed or not
for service:

## Slide 4: There are problems with this approach
Heavy reliance on inspection and testing is expensive
It creates an adversarial relationship between the Supplier (who wants looser specifications) and the Customer (who wants tighter specifications)
It encourages an attitude of “just good enough”
It does not address the problem of bad product being made in the first place
People often resort to defining “acceptable number non-conforming to specification” (which is an evil concept to us in SPC)

## Slide 5: The Statistical Approach
Remember that no two products are exactly alike
Begin by accepting this fact and that there is a natural variability present in any production (or service) setting
Minimize the variation within the process
Improve the process, do not rely exclusively on sampling to insure quality

## Slide 6: Basically two sources of variation within any process
Common Cause variation: If the process is running as designed and implemented, some level of variation will always be present. This is Common Cause.
Special Cause variation: Any variability present within the process which is not inherent to the process. This is Special Cause.
If a process exhibits the presence of Special Cause variation, the root causes are to be found and removed.
This is one of the main foundations of Statistical Process Control (SPC).

## Slide 7: Does this mean we get rid of Specifications or sampling?
Short answer, no.
Sampling will always be required to monitor a process to detect the presence of Special Cause.
Once Special Cause has been removed, it then makes sense to compare Process performance to Specifications since they reflect Customer requirements.
First it is necessary to define the Process and what is to be measured for monitoring purposes.

## Slide 8: How do we proceed?
Standardize the Process.
Monitor and remove Special Cause Variation.
Compare performance of the stable Process (Process without Special Cause) to customer requirements (beginning with Specifications).
Continually improve the process within your QMS-Quality Management System.

## Slide 9: What constitutes a QMS?
Any Quality Management System must satisfy four requirements:
Processes must be defined and their procedures appropriately documented.
Processes are fully deployed and implemented as stated.
Processes are effective in providing the expected results.
An Improvement System must be in place to improve Processes.